## Slide 1: GOAL
The goal of the study is to improve the classification accuracy of MI data for BCI systems and also to investigate whether the LS-SVM with tunning hyper parameters is better as a classifier than a logistic regression or kernel logistic regression classifier with cross-correlated features in an EEG-based MI classification.
A novel algorithm CC-LS-SVM,is proposed where a CC technique is developed for feature extraction and a LSSVM is employed for classifying the obtained features. The performance of the LSSVM classifier is compared with a logistic regression classifier and a kernel logisticregression classifier for the same feature vector set

## Slide 2: Advantages of the proposed algorithm
The LS-SVM is a robust intelligent technique for classification in BCI applications.
It has the advantage over other techniques of converging to a global optimum, not to a local optimum that depends on the initialization or parameters affecting the rate of convergence.
The computation of the LS-SVM is faster compared with other machine learning techniques because there are fewer random parameters and only the support vectors are used in the generalization process

## Slide 3: The data sets
The proposed approach in this chapter is evaluated on datasets, IVa and IVb of BCI Competition III, where both sets contain MI EEG recorded data.

## Slide 4: Basic steps for any algorithm
EEG signals
of two
classes
Feature extraction using cross-correlation
Classification using different algorithms
10-fold cross validation
Classification outcomes

## Slide 5
One Reference signal
All the non-reference signals
Cross- correlogram
EEG signals of two classes
Statistical feature extraction
Cross-correlation

## Slide 6
One reference signal
All the non-reference signals
EEG signals of two classes
Cross-correlograms
Statistical feature extraction
Cross-correlation

## Slide 7: Cross-correlation and statistical feature extraction
A cross-correlation sequence, denoted by ‘Rxy’, is calculated recursively using a reference signal and any other non-reference signal using the cross-correlation technique .
The graphical presentation of a cross-correlation sequence is called a cross-correlogram.
The reference signal of a class is crosscorrelated with the data of the remaining signals of this class and the data of all signals of another class.
If we have two classes of EEG signals, and class 1 has n signals and class 2 has m signals, and a reference signal is chosen from class 1, then a total of (n-1) cross-correlation sequences are obtained from class 1 and a total of m cross-correlation sequences from class 2.
To reduce the dimensions of the cross-correlation sequences, this study considers six statistical features, mean, median, mode, standard deviation, maximum and minimum as the representatives ideally containing all important information of the original signal patterns.
These features are calculated from each crosscorrelation sequence or cross-correlogram to createfeature vector sets.
The six traits of the cross-correlation sequences are found to serve as important indicators of the neurological state of the subjects

## Slide 8: cross-validation
10-fold cross-validation method is used for assessing the performance of any method. This procedure divides the feature vector sets into ten approximately equal-sized distinct partitions.
One partition is then used for testing, whilst other partitions are used for training the model.
To further improve the estimate, the procedure is repeated ten times and all accuracy rates over these ten runs are averaged.
The average accuracy over the ten runs obtained from the test data is taken as the performance evaluation criteria in this study

## Slide 9: Prime techniques of classification
LS-SVM
LR
KLR

## Slide 10: Classification by ls-svm
LS-SVM is employed with radial basis function (RBF) kernel as a classifier to distinguish the features obtained from the cross-correlation technique.
The obtained training feature vector of six dimensions are used as the input to train the LS-SVM classifier and the testing feature vector sets are employed to verify the performance and the effectiveness of the trained LS-SVM for the classification of two-class of EEG signals in the both datasets.
The two important parameters of the LS-SVM are selected by a two-step grid search technique for getting reliable performance of the method.
Classification using LS-SVM technique is employed using the standard function present in the LS-SVM toolbox
The classification accuracy is measured using the 10 fold cross validation technique

## Slide 11: Classification by LR
To compare the performance of the proposed LS-SVM classifier, we employ the logistic regression classifier instead of the LS-SVM for the same feature sets as its inputs.
The parameters of LR are estimated by maximum likelihood estimation (MLE)
LR technique is employed using “glmfit” and “glmval” functions present in matlab.
The classification accuracy is measured using the 10 fold cross validation technique.

## Slide 12: Classification by KLR
LS-SVM is also compares with a kernel logistic regression classifier.
Kernel logistic regression is a nonlinear form of logistic regression. It can be achieved via the so-called “kernel trick” which has the ability to classify data with nonlinear boundaries and also can accommodate data with very high dimensions.
the parameters of this method are automatically estimated by iteratively re-weighted least square procedure
the performance of the algorithm is evaluated through a 10-fold cross-validation procedure.
This algorithm is employed using the “minFunc” and also the package provided by mark Schmidt http://www.di.ens.fr/~mschmidt/Software/code.html

## Slide 13: results
Subject | LS-SVM | LR | KLR
aa | 99.130435 +- 1.833204 | 97.122178 +- 2.557142 | 97.445652 +- 3.006555
al | 93.913043 +- 6.859223 | 65.931422 +- 4.468074 | 92.860672 +- 5.181916
av | 99.565217 +- 1.374903 | 97.842556 +- 3.063261 | 98.731884 +- 2.042456
aw | 97.468944 +- 3.000330 | 96.943700 +- 4.412244 | 95.324440 +- 4.135244
ay | 93.711180 +- 3.289296 | 70.841416 +- 4.844978 | 89.362648 +- 7.511496
Thus from above we can conclude that LS-SVM is better that the other two

## Slide 14: Feature scaling +same indices
 | Lssvm | Lr | Klr | Mlp | Pnn | Multi
Aa | 99.130435 +- 2.749807 | 97.015272 +- 4.904171 | 97.445652 +- 2.949000 | 97.463768 +- 4.084912 | 92.318841 +- 4.769538 | 
For feature scaling I have changed the feature_extraction function and removed the extra scaling term form each algorithm
Same idices…changed did the same as above and also removed the indices term in each case

## Slide 15: Error can be 1 or 0
 | Lssvm | Lr | Klr | Mlp | pnn | multiclass
aa | 99.565217 +- 1.374903 | 97.463768 +- 4.042738 | 97.368248 +- 4.350160 | 98.712121 +- 2.076243 | 95.665349 +- 4.675504 | 
al | 94.503106 +- 4.517184 | 68.104414 +- 4.296824 | 91.521739 +- 6.010684 | 94.909420 +- 3.897104 | 87.717391 +- 8.533017 | 
av | 99.565217 +- 1.374903 | 97.047101 +- 2.831153 | 98.713768 +- 2.071617 | 98.731884 +- 2.042456 | 98.731884 +- 2.042456 | 

## Slide 16
Pre-processing
Feature extraction
Feature selection
Feature classification
EEG recording
Classification outcomes

## Slide 17: Along with 99 and c3 reference
 | Lssvm-fp1 |  | Lssvsm-c3 |  | Lr-fp1 |  | Lr-c3 |  | Klr-fp1 |  | Klr-c3 | 
 | 666 | 999 | 666 | 999 | 666 | 999 | 666 | 999 | 666 | 999 | 666 | 999
Aa | 99.13 | 100 | 100 | 100 | 97.04 | 99.58 | 98.29 | 100 | 97.06 | 99.14 | 98.71 | 100
Al | 94.34 |  |  |  | 69.29 |  |  |  | 91.95 |  |  | 
Av |  |  |  |  |  |  |  |  |  |  |  | 
Aw |  |  |  |  |  |  |  |  |  |  |  | 
Ay |  |  |  |  |  |  |  |  |  |  |  | 
avg |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 18: Contn…
 | MLP-FP1 |  | MLP-C3 |  | PNN-FP1 |  | PNN-C3 |  |  |  |  | 
 | 666 | 999 | 666 | 999 | 666 | 999 | 666 | 999 |  |  |  | 
 | 96.19 | 99.56 | 99.14 | 100 | 97.06 | 99.14 | 99.13 | 100 |  |  |  | 

## Slide 19
 | Lssvm-fp1 |  | Lssvsm-c3 |  | Lr-fp1 |  | Lr-c3 |  | Klr-fp1 |  | Klr-c3 | 
 | 999 | 666 | 666 | 999 | 999 | 666 | 999 | 666 | 999 | 666 | 999 | 666
Aa | 100 | 99.20 | 100 | 100 | 99.58 | 97.46 |  | 97.46 | 98.71 | 97.88 |  | 98.71
Al |  | 94.34 |  |  | 86.39 | 63.60 |  | 80.43 | 91.54 | 92.84 |  | 88.49
Av |  | 99.13 |  |  | 95.72 | 96.14/95.72 |  | 91.97 | 94.90 | 95.74 |  | 94.07
Aw |  | 98.26 |  |  | 96.17 | /91.82 /96.14 |  | 99.13 | 94.81 | 95.32 |  | 97.42
Ay |  | 90.51 |  |  | 70.21 | 66.25/71.46 |  | 65.38 | 84.25 | 84.63 |  | 79.51
avg |  |  |  |  |  |  |  |  |  |  |  | 
USING ARSENAL
d
d

## Slide 20
signal
cA1
cD1
cA2
cD2
cA3
cD3
LP
LP
LP
HP
HP
HP